## Slide 1: Tutorial 3: Mastering Organic Matter Analysis through Fourier-transform Ion Cyclotron Resonance (FTICR) Mass Spectrometry Data Processing.
Will Kew
Chemist
william.kew@pnnl.gov
November 7th, 2023

## Slide 2: Brief Recap
This Session

## Slide 3: Raw Data Processing
For reference only!
MONet will do this process
Time domain to Mass Domain
Peak Picking
Mass Recalibration
Formula Assignment

## Slide 4: Raw Data in FTICR – Time Domain
Time domain signal is recorded (‘transient)
Transient is ‘apodized’ (window function applied)
Transient is ‘zero-filled’
Transient is Fourier transformed to the ‘frequency domain’
This is almost always done ‘behind the scenes’
FFT
zf

## Slide 5: Raw Data in FTICR – Frequency to Mass Domain
Frequency domain spectrum
This is almost always done ‘behind the scenes’
m/z domain spectrum
Instrument specific calibration function
Note – Every instrument has its own specific calibration function coefficients
For FTICR instruments, the frequency (and thus m/z) depends on the magnetic field strength
Higher magnetic field = higher frequency = higher mass resolution

## Slide 6: Noise Thresholding and Peak Picking in FTMS
Next, we process the spectrum to extract the information about the peaks
Noise thresholding
  Determination of the spectrum noise level
  User defined level above which to accept signals as ‘real’
    ‘signal-to-noise’ ratio (SNR, S/N)
Peak picking (centroiding)
  Determination of each peaks properties
    m/z
    Intensity (peak height)
    Resolution (width of peak)
    Signal-to-noise ratio
Noise Threshold
Noise Level
Real peak
This is almost always done ‘behind the scenes’

## Slide 7: Noise Thresholding and Peak Picking in FTMS
High resolution data
Resolving Power is commonly used to describe the width of a peak
  Resolution and Resolving Power are incorrectly used interchangeably
e.g. m/z / FWHM = R.P.
  FWHM = 0.001
  m/z = 351.00
  Resolving Power = 351,000
Resolution = full width at half max
Intensity = y-axis maximum
m/z = center of the peak on x-axis
This is almost always done ‘behind the scenes’

## Slide 8: Mass Recalibration
The measured m/z values are often not exactly correct
  Ion frequency shifts due to instrument drift, ‘space-charge’ effects, etc.
Almost always we will internally re-calibrate each spectrum
  ‘External Calibration’ = instrument default calibration
  ‘Internal Calibration’ = using known features within a spectrum to refine its calibration
Can use spiked in compounds, common contamination ions, or known endogenous molecules
  For water extract SOM, we use expected CHO formula
Residual ‘error’ should be <1ppm
Before recalibration:
Mean error is ~2ppm
Spread of errors is ~3ppm
After recalibration:
Mean error is ~0ppm
Spread of errors is ~0.5ppm

## Slide 9: Formula Assignment
All isotopes have an exact mass
  Known accurately to several decimal places
We have a ~1ppm uncertainty on our measured m/z values
We allow for certain ‘chemically plausible’ heuristics, for example:
  Organic molecule: C > 1, H > 4
  Negative ESI of NOM, O > 0
  Not many N, S, P (N < 3, S<2, P < 1)
  No other heteroatoms
  [M-H]- ion type
Calculate all possible combinations of atoms which give us the measured m/z value

## Slide 10: Formula Assignment
Obviously, we use software to do this – for example, a web app called ChemCalc
https://www.chemcalc.org/mf-finder
For this mass, only one formula is within 5 ppm – thus, we have our ‘unambiguous assignment’

## Slide 11: Formula Assignment
Or we can use commercial software, like Bruker DataAnalysis
At higher m/z values, the number of possible assignments within 1ppm becomes greater!
Here, the third option (C22H19O14) is most likely correct
  Chemistry – an N14 molecule is unlikely!
  Sample + MS knowledge

## Slide 12: Formula Assignment
Formula Assignment is not an exact science
In complex mixtures, there is always some uncertainty
  Multiple possible formulas within the mass tolerances
  Insufficient resolution
  Too many elemental possibilities
    Especially when we include CHNOSP and multiple ion types (e.g. [M-H]- and [M+Cl]-)
Historic convention
  Pick a single ‘best match’
Modern approach
  “Embrace the ambiguity”
  Sometimes, one peak is multiple formulas

## Slide 13: Formula Assignment and Isotopologues
Confidence Scores (CoreMS)
Combines m/z error and isotopic pattern
Note, we observe not just the monoisotopic species, but isotopologues too, e.g.
  Monoisotopic: 12C6 1H12 16O6
  A+1 Isotopologue:
    13C1 12C5 1H12 16O6
    12C6 2H1 1H11 16O6
    12C6 1H12 17O1 16O5
  [C6H12O6-H]-
13C112C51H1216O6
12C62H11H1116O6
12C6 1H1217O116O5
180.058369
180.059232
180.061291
If we detect the predicted isotopologues, our confidence in the molecular formula is increased

## Slide 14: Data ‘Alignment’
Combining datasets – for comparative analysis – can be done two ways:
  1) Alignment based on m/z prior to assignment (e.g. Formularity)
  2) Alignment based on assigned formula (e.g. CoreMS)
Both approaches have their limitations
  1) Alignment based on m/z assumes that similar (e.g. within 1 ppm) m/z values between samples are the same species
    This is a big assumption.
    Can artificially align features which shouldn’t be
  2) Alignment based on Formula is more robust, but unassigned features can not be aligned and thus not compared
    Unassigned features may still contain useful information
179.0811
179.0820
179.0815
Feature A
179.0811
179.0820
179.0815
Formula
Formula
Formula
Formula
Feature A
Alignment on masses
Alignment on formulas

## Slide 15: Software for Data Processing
github.com/EMSL-Computing/CoreMS
Yuri E. Corilo, William R. Kew, Lee Ann McCue (2021, March 27). EMSL-Computing/CoreMS: CoreMS 1.0.0 (Version v1.0.0), as developed on Github. Zenodo. http://doi.org/10.5281/zenodo.4641553
EMSL developed software framework for mass spectrometry data processing
Open Source
Python based
End-to-end workflows
Raw data support
Modular and extensible
GUI, CLI, and Code-level access
Other software tools exist, including:
Bruker DataAnalysis (proprietary)
Formularity (EMSL, .exe)
  Mass calibration and formula annotation
MFAssignR (MTU, R-based)
  Noise thresholding, mass cal., formula annotation
UltraMassExplorer (AWI, web-based/R)
  Formula annotation

## Slide 16: Output from the Data Processing Step
Long-form table of peaks detected in the spectrum
Includes measured properties
  e.g. m/z, peak height, S/N
Includes assigned formula properties
  e.g. formula, mass error, confidence score, DBE, O/C and H/C, class

## Slide 17: Data Analysis and Interpretation
Typical spectrum metrics
Stoichiometric Properties
  Aromaticity
  Thermodynamics
  Chemical Classification
Data Visualization
Statistical Analysis
Peak Intensity Usage
Software Tools and Training

## Slide 18: Spectrum Metrics
Every spectrum has some basic metrics we often report or highlight
For Example:
  Total number of peaks
    9441
  Total number of assignments
    3507
  r.m.s of m/z recalibration (ppm)
    0.12
  m.a.e of m/z of assignments (ppm)
    0.11
  Total Ion Current (TIC)
    2x108
  Skewness of m/z distribution
    0.266
Spectrum of Suwanee River Fulvic Acid
Distribution of #O atoms in each assignment

## Slide 19: Stoichiometric Analysis
Elemental ratios allow us to predict some molecular properties
These allow us to infer biogeochemical traits
At simplest, the ratio of H/C can estimate saturation
  Methane = CH4. H/C = 4 = Saturated
  Benzene = C6H6. H/C = 1 = Unsaturated
Other elemental ratios can be calculated
Combinations of elemental ratios can yield more sophisticated inferences
m/z
m/z 195.08765
[C8H10N4O2 + H]+
Stoichiometric Analysis
H/C = 1.25
O/C = 0.25
DBE = 8
AImod = 0
NOSC = 0.75
Caffeine

## Slide 20: Data Visualization – Van Krevelen Diagrams
Van Krevelen diagrams are one of the most common ways to present complex mixture FTICR MS data
  Named after Dirk van Krevelen’s work in the 1950s
  van Krevelen, D.W. (1950). "Graphical-statistical method for the study of structure and reaction processes of coal", Fuel, 29, 269–84
Modern usage plots every assigned formula on a 2D scatter plot with O/C (x-axis) vs H/C ratio
  Less commonly, N/C instead of O/C
Regions of the plot can be used to infer chemical class
  n.b. – many class definitions are overly simplistic
Many of the most used definitions do not require ‘aminosugar’ or ‘protein’ species to contain N!
Regardless of definition set used – recall these are ‘class-like’ compounds
e.g. ‘lipid-like’ or ‘lignin-like’
Example van Krevelen diagram of a soil extract

## Slide 21: Chemical Classification from Van Krevelen Space
J. Am. Soc. Mass Spectrom. 2022, 33, 1, 198-202
Anal. Chem. 2018, 90, 10, 6152-6160
Phytochemical Analysis. 2022;33:1111–1120

## Slide 22: Van Krevelen Diagrams - Continued
Renaissance of van Krevelen diagrams started in the early-2000s
  Anal. Chem. 2003, 75, 5336
  Anal. Chem. 2004, 76, 2511
Extended ways to visualize the data have been presented
  Color coding the glyphs
  Size coding the glyphs
  3D plots
    (avoid in publication!)
  Interactive plots
Rapid Commun Mass Spectrom. 2017, 31 (7): 658–662.
Journal of the American Society for Mass Spectrometry. 2017, 28 (1): 200–213
Example van Krevelen diagram for Suwanee River Fulvic Acid standard

## Slide 23: Van Krevelen Diagram – Example Molecules
Chlorogenic Acid
Ellagic Acid
N-Acetylglucosamine
Leucine
Palmitic Acid
Caffeine
C16H18O9
C8H15NO6
C14H6O8
C6H13NO2
C16H32O2
C8H10N4O2

## Slide 24: DBE – Double Bond Equivalents
Equation
Interpretations
  Represents a sum of rings + unsaturated bonds in a molecule
  Often normalized to number of C
    e.g., DBE/C or DBE v C plots.
Limitations
  Does not include oxygen – a major part of NOM!
Citation
  Rapid Comms. Mass. Spectrom., 2006, 20, 5, 926-932
C16H18O9,
mw = 354 Da
Chlorogenic Acid
N-Acetylglucosamine
C8H15NO6,
mw = 221 Da
Ellagic Acid
C14H6O8,
mw = 302 Da
DBE = 8
DBE/C = 0.5
DBE = 12
DBE/C = 0.86
DBE = 2
DBE/C = 0.25

## Slide 25: Data Visualization – DBE
DBE vs C for a single sample – each assigned formula is a point
Distribution of DBE values between two samples of two different depths
Deeper samples (bottom) have higher DBE – more unsaturation

## Slide 26: AI – Aromaticity Index
Equations
Interpretation
  AI > 0.67 = Condensed Aromatic
  AI > 0.5 = Aromatic
  AI < 0.5 = Aliphatic
Limitation
  Indicates a molecule-average property
  Assumptions about bonding of O and other heteroatoms
  AIcon requires more knowledge of the sample chemistry
Citation
  Rapid Comms. Mass. Spectrom., 2006, 20, 5, 926-932
  Rapid Comms. Mass. Spectrom., 2016, 30, 1, 250-250
  Environ. Sci. Technol. 2022, 56, 4, 2729–2737
n.b. typo in the original publication, first two equations are based on the corrected article
AI is constrained between 0 and 1
C16H18O9,
mw = 354 Da
Chlorogenic Acid
N-Acetylglucosamine
C8H15NO6,
mw = 221 Da
Ellagic Acid
C14H6O8,
mw = 302 Da
AI = 0.0 (aliphatic)
AImod = 0.3 (aliphatic)
AI = 0 (aliphatic)
AImod = 0 (aliphatic)
AI = 0.67 (aromatic)
AImod = 0.80 (cond. aromatic)

## Slide 27: NOSC – Nominal Oxidation State of Carbon
Equation
Interpretation
  Estimate of (bio)energetic potential of compounds based on their elemental composition
  Rationalization of persistence and degradation of NOM
Limitation
  Thermodynamics without structural information has inherent uncertainties
Citation
  Geochimica et Cosmochimica Acta, 75, 8, 2011, 2030-2042
C16H18O9,
mw = 354 Da
Chlorogenic Acid
N-Acetylglucosamine
C8H15NO6,
mw = 221 Da
Ellagic Acid
C14H6O8,
mw = 302 Da
NOSC = 0
NOSC = 0.71
NOSC = 0
Leucine
NOSC = -1.0
C6H13NO2,
mw = 131 Da
Palmitic Acid
C16H32O2,
mw = 256 Da
NOSC = -1.75

## Slide 28: Data Visualization – AImod
Distribution of AImod values between two samples of two different depths
This shows a different story to DBE!
Here the shallower depth (top) contains a broader distribution of AImod values, including more condensed aromatic species
Aliphatic
Condensed aromatic
Aromatic
AImod vs C for a single sample
This is a ‘hex-binned’ density plot, showing the values of each assigned formula, but aggregated by count
Top and Right projections show 1D histograms
Aliphatic
Aromatic
Condensed aromatic

## Slide 29: NOSC
Biogeochemistry (2016) 127:157–171
Estimated NOSC values for various SOM components
= NOSC
Front. Soil Sci., 14 April 2023 Sec. Soil Biogeochemistry & Nutrient Cycling Volume 3 - 2023 | https://doi.org/10.3389/fsoil.2023.1120425
Notes: Biogeochemistry (2016) 127:157–171

## Slide 30: Cox Gibbs Free Energy (, GFE)
C16H18O9,
mw = 354 Da
Chlorogenic Acid
N-Acetylglucosamine
C8H15NO6,
mw = 221 Da
Ellagic Acid
C14H6O8,
mw = 302 Da
Equation
Interpretation
  Estimate of thermodynamic energy of the organic molecule
  Units of kJ(mol C)-1
Limitation
  Coefficients to estimate it from formula uses NOSC and empirically derived values (at 25 °C, 1 bar)
    These may not hold true in all cases
Citation
  Geochimica et Cosmochimica Acta, 75, 8, 2011, 2030-2042
GFE = 60.3
GFE = 60.3
GFE = 39.9
Leucine
GFE = 110.2
C6H13NO2,
mw = 131 Da
Palmitic Acid
C16H32O2,
mw = 256 Da
GFE = 88.8

## Slide 31: Comparing Datasets – Between Time and Instrument
Reproducibility and repeatability of direct infusion FTMS is a perennial question
Correcting for batch effects is not a solved problem
Interlaboratory studies do provide some guidance on comparisons
Limnol Oceanogr Methods, 18: 235-258. https://doi.org/10.1002/lom3.10364
Same standards run in ~20 labs
Some ions common to most, some aren’t.

## Slide 32: Statistical Analysis
Statistical comparison can take many forms
Unsupervised methods
  e.g. PCA, PCoA
  using formula-level info (intensity, presence-absence)
Traditional methods on aggregated properties
  e.g. t-tests or ANOVA on NOSC values
Appropriate statistical analysis requires careful consideration of:
  Experiment design
  Normalisation
  Validation
Limnol Oceanogr Methods, 18: 235-258.
Principal coordinate analysis
Nature Geosci 10, 415–419 (2017).
Welch’s unbalanced t-test

## Slide 33: Peak Intensities
Mass spectrometry peaks are not of arbitrary intensity
However, the features are not directly quantitative of the amount of that material in the original sample
Use of peak intensities must be done very cautiously!
Sources of Non-Quantitative Peak Intensities
Extraction Biases
SPE Biases
Matrix Effects
Ionization Efficiency
Ionization Suppression
Instrumental Biases

## Slide 34: Peak Intensities
Comparing different peak intensities within the same spectrum = never quantitative
Comparing the same peak between spectra = can have quantitative value, but often must be used very cautiously
Reviews and syntheses: Use and misuse of peak intensities from high resolution mass spectrometry in organic matter studies: opportunities for robust usage
https://egusphere.copernicus.org/preprints/2022/egusphere-2022-1105/
doi:10.5194/egusphere-2022-1105

## Slide 35: Peak Intensities – Pure Compounds, Idealised Case
Direct infusion of three different chemicals, individually, at the same concentration shows massive differences in relative signal intensity
Even here using three isomeric compounds, they yield massive differences in relative signal intensity
If we only know molecular formula, we don’t know – for sure – the same formula is the same molecule in different samples – so even comparing the same peak can be difficult in otherwise ideal situations
Reviews and syntheses: Use and misuse of peak intensities from high resolution mass spectrometry in organic matter studies: opportunities for robust usage
https://egusphere.copernicus.org/preprints/2022/egusphere-2022-1105/
doi:10.5194/egusphere-2022-1105

## Slide 36: Peak Intensities – Mixture, Complex Matrix
Reviews and syntheses: Use and misuse of peak intensities from high resolution mass spectrometry in organic matter studies: opportunities for robust usage
https://egusphere.copernicus.org/preprints/2022/egusphere-2022-1105/
doi:10.5194/egusphere-2022-1105
Known compounds at fixed concentration
Spiked into different matrices
  Methanol, SPE-eluted methanol, Salted SPE eluted methanol
With varied concentrations of SRFA added
Each compound behaves differently
Different matrices yield different responses
Direct use of peak intensity data in real samples, with complex and variable matrices, is not encouraged
However…

## Slide 37: Peak Intensities – Aggregated Properties
Reviews and syntheses: Use and misuse of peak intensities from high resolution mass spectrometry in organic matter studies: opportunities for robust usage
https://egusphere.copernicus.org/preprints/2022/egusphere-2022-1105/
doi:10.5194/egusphere-2022-1105
Direct use of peak intensity data in real samples, with complex and variable matrices, is not encouraged
However, there seems to be some cases where aggregating spectrum properties with some intensity ‘weighting’ can yield valid interpretation.
Possibly, due to the law of large numbers – where comparing one peak intensity isnt valid, across hundreds or thousands, properties ‘average out’
Here – we simulated a dataset of 100 or 1000 peaks, and added random error to the peak intensities.
We then calculated various metrics (e.g. α- or β-diversity)
With larger datasets, the calculated metrics reflect the true values
Much more work is required in this area to develop robust guidance

## Slide 38: Software for Data Analysis
PyKrev
  Python library for downstream analysis
  J. Am. Soc. Mass Spectrom. 2021, 32, 5, 1263–1267
  github.com/Kzra/pykrev
MetaboDirect
  R & Python based library
  github.com/Coayala/MetaboDirect
  Microbiome 11, 28 (2023)
ftmsRanalysis
  R based toolkit for downstream analysis
  github.com/EMSL-Computing/ftmsRanalysis
  PLoS Comput Biol 16(3): e1007654
FREDA
  Shiny web app for downstream analysis
  https://shinyproxy.emsl.pnnl.gov/app/freda
  github.com/EMSL-Computing/FREDA
Each tool has various strengths depending on data analysis Qs

## Slide 39: Software for Data Analysis – Shiny App
https://shinyproxy.emsl.pnnl.gov/app/1000soils

## Slide 40: Introduction to Session 4
In our ‘Hands-On’ session, we will practice exploring real SOM FTICR datasets
  Calculating metrics
  Visualizing data
  Comparing samples
We will use basic Jupyter Notebooks
Explore the code yourself:
github.com/EMSL-MONet/CommSciMtg_Nov23/

## Slide 41: Questions?
william.kew@pnnl.gov

## Slide 42: Thank you